## Slide 1: Drone detection
Introduction, motivations, scenario description
How it is possible to detect a drone?
Radar solutions and state of the art
Design of radar parameters, FMCW case
Micro Doppler introduction
Future plans

## Slide 2: Motivations
Growth of incidents due to unauthorized drones:
Airport (Gatwick 2018), ISIS attacks with DJI Phantom bougth on Amazon (Syria 2016), Attempt to Venezuelan president Maduro (2018)
Low cost and ease of use, Off the shelf technology
Rapid technological evolution due to large benefits in several fields, agriculture engineering, package delivery, security

## Slide 3: Environment
1. Military environment:
Complexity and expensive system of military level
2. Civil environment:
Low cost, simple and portable systems or fixed solutions
Airport, public institutions
Buildings, power plants, prisons
Crowded squares, public events
We select this context, characterized by presence of near people, near radio-frequency services and security problems like:
Privacy violation, transport of illegal stuff, spy

## Slide 4: Anti Drone complete system
Detection solutions
Thermal Optic/IR cameras
Radio Frequency RF scanner
Radar FMCW radar
Sound Acoustic sensors
 Hybrid is the most complete system
Phase 1: Detection + Recognition
Phase 2: Identification + Risk level
Phase 3: Neutralization
Range of hunderd of m
Privacy
Autonomous flight
Noise env.
Very short range
More complete solution

## Slide 5
Difficulties and Goal
Drones are advanced and mature technology
Very small dimension, RCS = 0.01 - 0.03
Velocity from 50 km/h to 140 km/h
Maximum range of about 10 km from controller
Altitude of about 6 km
Design a radar capable to detect and recognize this type of UAV with
Goal:
- Low cost HW
- Low power TX
- Small dimensions
- Easy to deploy

## Slide 6: Actual solutions
Above 8 GHz frequency bands
Good result achieved with FMCW radar
Recognition with Micro Doppler analysis
Transmitted power tens of Watt
Maximum detection range of 4 km
Mosts are based on:

## Slide 7: FMCW Radar parameters: distance
In order to dimension some parameters of FMCW radar
Chirp signal
Sampling frequency must be almost equal
to maximum IF frequency related to d max
Distance resolution is only related to the bandwidth
Where B is equal to:
2D FFT is performed to measure distance and velocities, on fast time and short time plane
IF frequency is the output of mixing tx signal and rx signal

## Slide 8: FMCW Radar parameters: B, S, Tc
Same B means same distance resolution,
But varying S and Tc is possible to:
A. Lower sampling frequency , lower IF bandwidth, means low cost ADC converter but lower maximum distance
B. Double slope, double sampling frequency, but half measurements time and higher maximum distance

## Slide 9: FMCW Radar parameters: velocities
In order to measure velocities, phase difference among N chirps must be computed
Unanmbiguos velocity measurement, phase change must be minus than pi
Velocity resolution is related to the frame time of FFT
Where Tf is equal to:
N is the number of chirp transmitted
A. Double N, half Tc means higher velocities measurable
B. Half N, double Tc means lower velocities measurable
Same velocity resolution but:

## Slide 10: Some values of actual solutions
Considering the radar Surveillance Equation:
ART mid range 3D:
ELVIRA:
IRIS:
s
(Assuming L = 0 dB, Ts = 290K)
s
s

## Slide 11: Micro Doppler
When an object is moving, backscattered signal is shifted by
If the object has any rotating or vibrating part --> additional frequency shift is induced
Different objects have different and unique micro doppler signature, so is possible to classify its
How is it possible to study it?
Fourier Transform is not capable to represent frequencies over time
Short Time Fourier Transform is an example of time-frequency distributions

## Slide 12: Micro Doppler
Considering a 3D model of a rigid body approximated by a single scatterer point
Target made a traslation from P to P’’ and then rotate from P’’ to P’
Rotations are represented by means of Euler angles by Rotation matrix, also called Roll, Pitch and Yaw matrix
For a target composed by multiple scatterer points the math became complex
Is possible to separate the contribution in frequency shift
Many approximations done: velocities much low than c, distance too large to consider EM in far field

## Slide 13: Micro Doppler
If we consider the temporal evolution of angular velocity, (Rodrigues formula), is possible to observe the evolution of frequency shift due to mD.
STFT, What is it?
Is like to do a FFT for each short time window

## Slide 14: Next phase
Complete study about Micro Doppler in radar, difference between Wideband and Narrowband radar signals
Backscatter signal model for drone
Micro Doppler specific features in FMCW radar

## Slide 15
Aumentando la durata del chirp diminuisco la frequenza di sampling, low cost adc
Il SNR finale è calcolato come l’integrazione di N segnali mandati sul target durante il dwell time (tempo speso sul tgt in una singola scansione)
Calcolo parametri radar con range più corto, quanta potenza mi serve?