## Slide 1
Contents
Micro-Doppler and time frequency analysis (short recap)
mD in Narrowband vs Wideband radar, ‘cell migration’ effect
Received signal model from rotor blades
Futures extraction from drone’s spectrograms
Mapping of features from spectrograms to radar waveform
Verification of mD constraints on range restricted (1 km) FMCW radar (with the same assumptions made for the mean power computation)

## Slide 2
Time frequency analysis
Goal: classification
Unique feature of a drone that can be observed in the time-frequency domain
Rotor blades
Typical signal in BB received from target
Approximating
Appl. Rodrigues Formulas

## Slide 3
Spectrogram
How to obtain it?
The choice of a suitable window is critical for time and frequency resolution, usually Hamming window is used
Wide window –> Lower time res and Higher freq. res
Narrow window –> Higher time res and Lower freq. res

## Slide 4
mD in Wideband radar
Radar time can be expressed as sum of slow time and fast time:
Time of received echo
(fast time)
Total time of tx (Slow time)
If we transmit a signal p(t), considering a target at distance R with a radial velocity v:
Approximated models
First order approx. -> (
Stop and go approx. -> (

## Slide 5
mD in Wideband radar
In case the radar transmit a LFM signal
The received echo from a target that has also
Rotational movements is :
In a FMCW, to extract frequency information
the dechirp operation is performed. RX signal is multiplied by complex conjugate of reference signal (the transmitted one)
Making Fourier Transform (considering
the beat signal is observed in short time)
It turn into a narrowband signal
Dependency on
Means mD effects is osservable also in range-slow time plane! And this led to Cell Migration effect on this plane
Echo from target (Stop and Go model):
[1]
[1]
[1] Changzhan Gu, and Jaime Lien,
Short Range Micro Motion Sensing whit Radar Technology. - Cap 5.2.2 - pag.123-124

## Slide 6
Cell Migration effect
In a LFMCW radar is not possible to use the Stop and Go model,
Neglecting what happens in intrapulse time led to relative large error such as Cell Migration effect, but…
This effect can be neglected?
If the ratio is possible to neglect it!
Considering the pulse compression of LFM, the doppler mismatch at output of MF led to cell migration effect
In our case (X-band) :
Typical velocities of a drone:

## Slide 7
Cell Migration effect
Considering a LMFCW radar, and by using Frist Order approximated model it’s possible to compute the migration due to the velocity of target
Received signal from target with
By dechirp operation:
It’s possible to compute frequency as usual by deriving the phase
Range scaling, by dividing
For we obtain a distance
From frequency
In our case (X-band) :
Displacement result in
About 3 millimeter
V of blades = 350 km/h
Dipende dai parametri del radar
Se uso un PRI di 1 ms forse si ha migrazione della cella
[2]
[2] QUN ZHANG, YING LUO, YONG-AN CHEN. MICRO-DOPPLER CHARACTERISTICS OF RADAR TARGETS. Cap. 3.4 – Pag.63-68

## Slide 8
Received signal model from rotor blades
Considering the follow reference system, in case of distance of blade tip from radar is:
(Taylor approx. + trigonometric formulas)
The received signal from it is:
Taking into account aspect angle, by integrating over the length of the blade, considering BB signal and neglecting some therm, we obtain:
At the end the doppler frequency is, as we expect:
with
By deriving the phase and using subtraction formulas of sin

## Slide 9
Received signal model from generic target
Considering the summation of each blades and each rotors and doppler frequency of body
If we compute now the spectrogram of this signal, considering only the rotations and neglecting of body
Vertical line are called Blade Flash:
When the blade is perpendicular to radar has its max value
Much closer blade flash, due to higher rotation rate
And consequent lower Tc

## Slide 10
Futures extraction from spectrogrm
Number of blades, if these are odd or even
Rotation rate of blades
Velocity of blade tip
Length of blade
Where Tc is the time distance between two blade flash
All these informations depends on measured Doppler Frequency, consequently only if there is sufficiently resolution in frequency and time its possible to see them!

## Slide 11
Radar parameters
In order to be able to capture all the informations relative to mD analysis, is possible to consider that it is necessary to observe at least 5 consecutive blade flashes
Translated into parameter requirements:
/5
/5
Mapping to FMCW radar
Due to shift of STFT window of
N/2 samples per time
M: Number of ramps on tgt
During an observation time
N: Number of samples
Of STFT window
Frequency resolution of SFTF, not
Overall
Another constraint come from maximum velocities measurements

## Slide 12
Verification of constraint
Taking into account the previous FMCW radar
designed parameters in power budget:
=
M
B
By extracting features from a real quad-drone spectrogram ( ,
By knowing
N = =10
Setting length of STFT window to 10, is equal to 500 Hz
Our is 55 ms
In order to see at least 5 consecutive blade flash:
From
/5 = 1 ms

## Slide 13
Next phases
Reduce as much as possible the requirements of radar
needed to see microdoppler effects
Spectrum analysis:
Mapping of microdoppler effects on the spectrum of received signals
Write steps done on thesis
Modello segnale ricevuto dalla pala, congiunzione tra I due modelli
Aggiugnere parametri al segnale
Matlab dati I parametri e I constraints restituisce forma d’onda compatibile
Ricerca modelli droni
Thanks for attention!