## Slide 1: Drone detection
Which kind of drones?
Low cost and ease of use
Benefit in agriculture engineering, package delivery, security
High diffusion among people
Growth of incidents due to unauthorized drones:
Airport (Gatwick 2018), ISIS attacks with DJI Phantom, Attempt to president Maduro
To better understand the goal:
1. Features of the subject to detect
2. Environment characteristic

## Slide 2: Features of the drones
Advanced and mature technology
Very small dimension, tens of cm
Velocity from 50 km/h to 140 km/h
Range of about 10 km from controller
Altitude of about 6 km
Tech difference with commercial drone defense
New and young technology

## Slide 3
Environment
1. Wide and high risk area:
Complexity and expensive system of military level
2. Civil environment:
Low cost, and simple system
We select this context
Airport, public institutions
Crowded squares, public events
Portable solutions
Fixed solutions
Buildings, power plants, prisons

## Slide 4
Environment
Radiowave environment
for detection considering
order of cm
Physical environment -> Multipath, blind zone (over certain height -> buildings, monuments)

## Slide 5
Detection solution
Thermal Optic/IR cameras
Radio Frequency RF scanner
Radar FMCW radar
Sound Acoustic sensors
Range of hunderd of m
Privacy
Autonomous flight
Noise env.
Very short range
More complete solution
But also radar has its limitations: Identification (Birds vs Drone), Tx license,Interference
Rotating parts (Micro doppler)
Spectrum analysis
 Hybrid is the most complete system!

## Slide 6
Complete system
1 Detection + Pre-Identification
2 ID + Valutazione del livello della minaccia
3 Neutralization
Rapid evolution of drones
-> Modular system
–> Upgradeable
Radar + EO camera
3
1
Jamming antennas
Leonardo Falcon Shield
2

## Slide 7
Possible solution for this purpose --> FMCW Radar
We can measure both velocity and distance
Low peak power trasmitted and LPI
Better distance resolution
Focus on radar solution

## Slide 8
Robin Radar solution -> IRIS
FMCW Solid State 3D radar
X-Band (8900-9650 MHz)
Detection range 4 km
Classification range 1.4 km
Azimuth accuracy 0.6°
Range accuracy 0.6 m
Classification method Micro doppler
Power 2x12 W (continuos)
State of art
Smaller
easy to deploy
Cost

## Slide 9
State of art
Robin Radar solution -> ELVIRA
FMCW Solid State 2D radar
X-Band (8700-9650 MHz)
Detection range 2.7 km
Classification range 1.1 km
Azimuth accuracy 1°
Range accuracy 0.6 m
Classification method Micro doppler
Power 4 W (Continuous)
Less small
2D
Less cost

## Slide 10
State of art
Aveillant solution -> Gamekeeper 16u
Holographic 3D radar
L-Band (1000-2000 MHz)
Detection range 7.5 km
Classification range 5 km
Peak power 2 kW
max altitude 900 m
Complexity
High cost

## Slide 11
State of art
Kelvin Hughes solution-> Spexer 360
Solid state pulse radar
X band 9.22 - 9.38 GHz
Peak power 80 W
Micro UAV (0.03^2 RCS) 2.4 km
Range accuracy RMS 5 m
Azimuth accuracy RMS 0.8°
Pfa 10^-4
Range resolution 28 m
Low resolution
High power

## Slide 12
State of art
Droneshield-> RadarZero
Metamaterial-based radar
K band (24.45 - 24.65 GHz)
Detection small drone range 750 m
Power 3.4 W
Main Beam Width 80° x 90°
Azimuth accuracy 1°
Low cost
1 km range

## Slide 13
SAAB solution -> Giraffe 1X
Stacked beam 3D radar
X-Band
Detection range small UAV 4 km
Power 2 kW
Radar weight <300 kg
State of art
Not so portable
High power
High cost

## Slide 14
Next Step
Analysis of literature FMCW radar solution for moving object
Choice the best useful technology for our case
Needs to satisfy:
  cm
  Velocity e range measurements
  Rotating parts to detect for identification (bird vs drone)
  Small dimension of antenna/radar -> portable
  Easy to deploy/use
  Low power/low cost

## Slide 15
RF scanners triangulation technique

## Slide 16
Vendor, Model | Combined techniques | Range
ELTA, Droneguard | Radar + RF scanner + Camera | 4.5 km
Aaronia, AARTOS DDS | Radar + Camera | 5 km
APS, Ctrl+sky | Radar + RF scanner + Camera + Acoustic | 3 km
Cerbari | RF scanner + camera | 3 km
Rodhe e Schwartz, Adronis | RF scanner | 3 km
Droneshield, Sentinel | Radar + RF scanner + Camera + Acoustic | 3.5 km

## Slide 17
Hijacking module
New attachment

## Slide 18
SPEC | IRIS | ELVIRA
Technology | FMCW | FMCW
Frequency | X-Band (8900-9650 MHz) | X-Band (8700-9650 MHz)
Power Output | 2 x 12 Watt | 4 Watt
Instrument Range | 5 km | 5 km
Detection Range | 4 km | 2.7 km
Classification Range | 2.2 km | 1.8 km
Main Beam Width | 6 ° x 60 ° | 10 ° x 10 °
Rotation | 30 rpm | 46 rpm
Classification Method | Micro-Doppler | Micro-Doppler
Range Accuracy | 0.6 m | 0.6 m
Azimuth Accuracy | 0.6 ° | 1 °

## Slide 19
Radar detection pro | Radar detection cons
Long range detection | Low RCS’s drone
Drone’s autonomous flight | Distinction from birds
Constant tracking | Transmission frequency license
Independence of visual condition | Interference
High accuracy localization | Low speed

## Slide 20
SPEC | Gamekeeper 16U
Technology | Holographic radar
Frequency | L-Band
Power Output | 2 kW
Instrument Range | 7.5 km
Detection Range | 5 km
Target RCS | 0.01
Range in Altitude | 900 m
Azimuth Coverage | 90 °
Elevation Coverage | 30 °
SPEC | Gamekeeper 16U
Technology | Holographic radar
Frequency | L-Band
Power Output | 2 kW
Instrument Range | 7.5 km
Detection Range | 5 km
Target RCS | 
Range in Altitude | 900 m
Azimuth Coverage | 90 °
Elevation Coverage | 30 °

## Slide 21
SPEC | Spexer 360
Technology | Solid State Pulse Radar
Frequency | X-Band [9.22-9.38 GHz]
Power Output | 80 W
Instrument Range | 2.4 km
Target RCS | 0.03
Range accuracy | 5 m RMS
Azimuth accuracy | 0.8 ° RMS
Azimuth Beam Width | <4.0°
Elevation Beam Width | 25 °
SPEC | Spexer 360
Technology | Solid State Pulse Radar
Frequency | X-Band [9.22-9.38 GHz]
Power Output | 80 W
Instrument Range | 2.4 km
Target RCS | 
Range accuracy | 5 m RMS
Azimuth accuracy | 0.8 ° RMS
Azimuth Beam Width | <4.0°
Elevation Beam Width | 25 °

## Slide 22
SPEC | Droneshield Radar Zero
Technology | -
Frequency | K band (24.45 - 24.65 GHz)
Power Output | 3.4 W
Instrument Range | 1 km
Target RCS | -
Range in Altitude | -
Azimuth Coverage | 80°
Elevation Coverage | 90°
Azimuth Accuracy | 1 °

## Slide 23
SPEC | FIELDctrl Access
Technology | 3D MIMO/AESA
Frequency | X-Band
Power Output | 2 kW
Instrument Range | 7 km
Detection Range | 2 km
Target RCS | 0.01
Range Accuracy/Resolution | 10 m / 6 m
Azimuth Coverage | 90 °
Elevation Coverage | 45 °
SPEC | FIELDctrl Access
Technology | 3D MIMO/AESA
Frequency | X-Band
Power Output | 2 kW
Instrument Range | 7 km
Detection Range | 2 km
Target RCS | 
Range Accuracy/Resolution | 10 m / 6 m
Azimuth Coverage | 90 °
Elevation Coverage | 45 °

## Slide 24
SPEC | ART midrange 3D
Technology | CWLFM
Frequency | Ku-Band [16 - 17 GHz]
Power Output | 15 W
Instrument Range | 10 km
Detection Range | 3 km
Target RCS | 0.01
Range Accuracy/Resolution | 0.25 m / 0.2 m
Azimuth Coverage | 360 °
Rotation | 60 rpm
Elevation Coverage | 1.3 °
SPEC | ART midrange 3D
Technology | CWLFM
Frequency | Ku-Band [16 - 17 GHz]
Power Output | 15 W
Instrument Range | 10 km
Detection Range | 3 km
Target RCS | 
Range Accuracy/Resolution | 0.25 m / 0.2 m
Azimuth Coverage | 360 °
Rotation | 60 rpm
Elevation Coverage | 1.3 °

## Slide 25
SPEC | Spexer 360 | Gamekeeper 16U | Droneshield Radar Zero | FIELDctrl Access | ART midrange 3D | IRIS | ELVIRA
Technology | Solid State Pulse Radar | Holographic radar | 2D Array | 3D MIMO/AESA | CWLFM | FMCW | FMCW
Frequency | X-Band (9.22-9.38 GHz) | L-Band | K band (24.45 - 24.65 GHz) | X-Band | Ku-Band (16 - 17 GHz) | X-Band (8900-9650 MHz) | X-Band (8700-9650 MHz)
Power Output | 80 W | 2 kW | 3.4 W | 2 kW | 15 W | 2 x 12 W | 4 W
Instrument Range |  | 7.5 km | - | 7 km | 10 km | 5 km | 5 km
Detection Range | 1.6 km (0.03 ) | 5 km (0.01 ) | 1 km | 2 km (0.01 ) | 3 km (0.01 ) | 4 km (0.03 ) | 2.7 km (0.03
Classification Range | - | - | - | - | - | 1.4 km | 1.1 km
Main Beam Width | 4 ° x 25 ° | 30 ° x 90 ° | 80° x 90° | 90° x 45° | 1.3° x - | 6 ° x 60 ° | 10 ° x 10 °
Rotation | - | - | - | - | 60 rpm | 30 rpm | 45 rpm
Class. Method | - | Proprietary algo. | - | - | Micro-Doppler | Micro-Doppler | Micro-Doppler
Range Accuracy | 5 m | - | - | 10 m | 0.25 m | 0.6 m | 0.6 m
Azimuth Accuracy | 0.8 ° | - | 1° | - | 0.2° | 0.6 ° | 1 °
SPEC | Spexer 360 | Gamekeeper 16U | Droneshield Radar Zero | FIELDctrl Access | ART midrange 3D | IRIS | ELVIRA
Technology | Solid State Pulse Radar | Holographic radar | 2D Array | 3D MIMO/AESA | CWLFM | FMCW | FMCW
Frequency | X-Band (9.22-9.38 GHz) | L-Band | K band (24.45 - 24.65 GHz) | X-Band | Ku-Band (16 - 17 GHz) | X-Band (8900-9650 MHz) | X-Band (8700-9650 MHz)
Power Output | 80 W | 2 kW | 3.4 W | 2 kW | 15 W | 2 x 12 W | 4 W
Instrument Range |  | 7.5 km | - | 7 km | 10 km | 5 km | 5 km
Detection Range |  |  | 1 km |  |  |  | 
Classification Range | - | - | - | - | - | 1.4 km | 1.1 km
Main Beam Width | 4 ° x 25 ° | 30 ° x 90 ° | 80° x 90° | 90° x 45° | 1.3° x - | 6 ° x 60 ° | 10 ° x 10 °
Rotation | - | - | - | - | 60 rpm | 30 rpm | 45 rpm
Class. Method | - | Proprietary algo. | - | - | Micro-Doppler | Micro-Doppler | Micro-Doppler
Range Accuracy | 5 m | - | - | 10 m | 0.25 m | 0.6 m | 0.6 m
Azimuth Accuracy | 0.8 ° | - | 1° | - | 0.2° | 0.6 ° | 1 °

## Slide 26
Type of drone | Velocity of body | Blade tip velocity
Quadcopter drone | 70 km/h | 226 km/h
Helicopter drone | 70 km/h | 345 km/h